## Slide 1: Chapter 2
Network topology

## Slide 2: Introduction
Overview:
  Network topologies define the physical or logical arrangement of nodes (devices) in a network.
  They determine how data flows and interacts between devices within a network.
  Different topologies offer varying benefits and drawbacks in terms of scalability, fault tolerance, and cost.
Key Points:
  Network topologies influence the performance, reliability, and manageability of a network.
  Choosing an appropriate topology depends on the specific network requirements and constraints.
  Common network topologies include bus, ring, star, mesh, and hybrid topologies.

## Slide 3: Why we need a topology
Choosing one topology over another can impact :
  type of equipment the network needs
  capabilities of the equipment
  network’s growth
  way a network is managed

## Slide 4: Bus

## Slide 5: Simple Physical Topologies
Characteristics:
  Devices are connected to a single central cable or backbone.
  Data travels in both directions along the cable, and all devices receive all transmissions.
  Terminators at the ends of the cable prevent signal reflections.
Applications:
  Small networks with a limited number of devices.
  Educational and home networks

## Slide 6: Bus (continued)
Devices share responsibility for getting data from one point to another
Terminators stop signals after reaching end of wire
  Prevent signal bounce
Inexpensive, not very scalable
Difficult to troubleshoot, not fault-tolerant

## Slide 7: Bus
Advantages
Simple and inexpensive to implement.
Easy to install and troubleshoot.
Disadvantage
Limited scalability and performance as the number of devices increases.
A break in the cable can disrupt the entire network.

## Slide 8: Ring

## Slide 9: Simple Physical Topologies
Characteristics:
  Devices are connected in a circular fashion, forming a closed loop.
  Data travels in one direction, passing through each device in the ring.
  Tokens are used to control data transmission, ensuring orderly communication.
Applications:
  Token Ring networks for reliable data transmission.
  Token Bus networks for distributed control and data flow.

## Slide 10: Ring
Advantages
Deterministic data flow, preventing collisions.
Fault-tolerant, as data can continue to flow if one device fails.
Disadvantage
Difficult to install and troubleshoot.
Adding or removing devices can disrupt the ring.

## Slide 11: Star

## Slide 12: Simple Physical Topologies
Characteristics:
  Devices are connected to a central hub or switch.
  Data is transmitted from the sender to the central device, which then broadcasts it to the intended recipient.
  Traffic is directed, reducing collisions and improving data transfer efficiency.
Applications:
  Local Area Networks (LANs) in offices and buildings.
  Ethernet networks for high-speed data transmission.

## Slide 13: Star
Advantages
Easy to install and manage.
Scalable to a large number of devices.
Fault-tolerant, as a central device failure doesn't affect the entire network.
Disadvantage
Relies on the central device for data transmission.
A central device failure can disrupt the network.
More expensive than bus or ring topologies.

## Slide 14: Mesh

## Slide 15: Mesh
Characteristics:
  Devices are interconnected in multiple redundant paths.
  Data can travel through multiple routes, providing high fault tolerance and flexibility.
  Routing algorithms are used to determine the optimal data paths.
Applications:
  Wide Area Networks (WANs) for large-scale networks.
  Wireless Mesh Networks for flexible and resilient connectivity.
  Peer-to-Peer (P2P) networks for distributed file sharing.

## Slide 16: Mesh
Advantages
Highly scalable and reliable.
Data can continue to flow even if multiple devices or connections fail.
Provides multiple paths for data transmission, reducing congestion.
Disadvantage
Complex to install and manage.
Requires more cabling and equipment.
Routing overhead can increase network latency.

## Slide 17: Hybrid Physical Topologies
Characteristics:
  Combines two or more basic topologies to create a hybrid topology.
  Provides the benefits of multiple topologies, addressing specific network requirements.
  Common hybrid topologies include star-bus, star-ring, and tree topologies.
Applications:
  Enterprise

## Slide 18: Hybrid Toplogy
Advantages
Flexibility to combine the strengths of different topologies.
Scalability and fault tolerance depending on the chosen hybrid topology.
Efficient data transmission for specific network scenarios.
Disadvantage
Complexity in design and implementation.
Potential compatibility issues between different topologies.
Increased cost compared to basic topologies.